You do not need to find external "real-world" experimental data for this. In computational physics, the standard way to validate a code is to compare it against an Analytical Solution (an exact mathematical formula).
Since your paper explicitly states that the random walk reproduces the diffusion equation where the distribution "approaches a Gaussian"1, you can use the Gaussian Probability Density Function as your "theoretical curve."
Here are two ways to generate this data yourself to validate your model.
1. The "Pulse Test" (Transient Validation)
This is the most rigorous test to prove your move probability calculation is correct.
The Theory:
If you release a pulse of heat packets at $(x=0, y=0)$ at time $t=0$, and let them diffuse without surface convection ($P_{conv}=0$) or boundaries, their distribution at any later time $t$ must follow a Gaussian curve (a Bell curve).
The Equation (Your "Theoretical Data"):
The theoretical temperature $T(r)$ at a distance $r$ from the center at time $t$ is:
$$T(r, t) = \frac{N}{4 \pi \alpha t} \exp\left( - \frac{r^2}{4 \alpha t} \right)$$
- $N$: Total number of packets.
- $\alpha$: The thermal diffusivity you used (e.g., for Copper: $1.1 \times 10^{-4}$ 2).
- $t$: The time of the snapshot (e.g., 1.0 seconds).
- $r$: The distance from the center.
How to do it in your code:
1. Modify: Turn off continuous injection ($Q$). Instead, start all 1500 packets at the center at $t=0$.
2. Run: Run the simulation for $t = 1.0$ second (500 steps).
3. Extract: Calculate the density of particles at different radii from the center.
4. Compare: Plot your simulation dots against the solid line generated by the equation above. If they overlap, your diffusion physics is perfect.
2. The "1D Slice" Test (Steady State Validation)
If you want to validate your final steady-state heat map (Figure 3), you can compare a cross-section of your plate to the theoretical decay.
The Theory:
For a 2D plate with surface cooling (Newton's law), the temperature drops off as you move away from the hotspot. Because you are using a square plate with absorbing boundaries3, the edges are forced to zero.
However, near the center (before hitting the edges), the decay should look like a Modified Bessel Function of the second kind ($K_0$). This is complex to calculate, but it behaves very similarly to an exponential decay in the middle range.
The Equation (Approximation):
Plot the natural logarithm of Temperature ($\ln(T)$) against the distance $r$.
$$\ln(T) \approx -C \cdot r + \text{constant}$$
How to do it:
1. Take your final data matrix (Figure 3).
2. Extract a single row of pixels going from the hotspot to the right edge.
3. Plot $\ln(T)$ vs Distance ($x$).
4. The Test: If the diffusion is working correctly, this line should be roughly straight (linear) near the center, before curving down rapidly as it hits the $T=0$ boundary at the edge.