Based on the current state of your paper, you have a solid "phenomenological" model—meaning you are successfully simulating the symptoms (harmonics, noise) without simulating the complex physics (contact mechanics) that causes them.
To elevate the quality of the assignment from "good" to "excellent," I suggest focusing on how the fault is modelled (making the signal more realistic) and how it is measured (using more sensitive metrics).
Here are three specific, high-impact improvements you could make:
1. Analysis Improvement: Add "Kurtosis" as an Indicator
Currently, you use RMS (Table 3 1), which measures the average energy. However, early-stage bearing faults produce sharp, short clicks that have high amplitude but low energy (because they are so short). RMS often fails to detect these early clicks because they get "averaged out."
Suggestion: Calculate the Kurtosis (the 4th statistical moment) of the signal.
- Why: Kurtosis specifically measures "spikiness." A healthy sine wave has a Kurtosis of 3. A signal with clicking faults will jump to 5, 10, or higher, long before the RMS value changes significantly.
- Implementation:
$$Kurtosis = \frac{\frac{1}{N} \sum (x[n] - \mu)^4}{\sigma^4}$$
2. Modelling Improvement: Simulate "Amplitude Modulation"
Your current model adds sidebands at fixed frequencies ($f_0 \pm 10$ Hz)2. In real machinery, these sidebands happen because the fault is rotating. As the defect moves in and out of the load zone, the vibration gets louder and quieter.
Suggestion: Instead of just adding a sine wave at $f_0 \pm 10$, explicitly model Amplitude Modulation (AM).
The Change: Multiply your high-frequency fault signal by a low-frequency envelope.
$$x_{fault}(t) = (1 + \sin(2\pi f_{mod} t)) \times \sin(2\pi f_{high} t)$$
Why: This demonstrates a deeper understanding of why sidebands appear (the physics of the load zone) rather than just placing them there arbitrarily.
3. Analysis Improvement: Envelope Analysis (Demodulation)
Your paper mentions "High-pass filtering" to isolate impact vibration3333. This is good, but the industry standard for this is Envelope Analysis.
+1
Suggestion: If you have time, perform a "Hilbert Transform" or simple "Rectification" on your high-pass filtered signal to extract the envelope.
- The Process:
  - High-pass filter the signal (keep only the high-frequency "ringing").
  - Rectify the signal (take the absolute value: $|x[n]|$).
  - Take the FFT of this rectified signal.
- Why: This is the "magic trick" of vibration analysis. It reveals the repetition rate of the clicks (the fault frequency) even if the clicks are buried in noise. Showing this spectrum alongside your standard spectrum would be a very advanced addition.
Summary of Recommended Next Steps
If you only have time for one change:
1. Easiest: Add Kurtosis to your "Quantitative wear indicators" section. It requires one line of code and adds a powerful new metric.
2. Most Impressive: Add Envelope Analysis (Rectified Spectrum). This is the standard tool used by actual vibration engineers and would make the analysis section much more professional.

If you want to significantly improve the grade, you don't need to rewrite the text. You need to add one advanced analysis technique to show you have gone beyond the basic requirements.
1. Add "Kurtosis" to Figure 5:
  1. Currently, Figure 5 shows RMS10.
  2. Action: Add a plot for Kurtosis. It is easy to calculate ($\frac{\text{mean of } x^4}{(\text{standard deviation})^2}$).
  3. Comment: "While RMS rose slowly, Kurtosis spiked immediately at light wear, proving it is a better early-warning indicator." This single insight shows deep critical thinking.
2. Mention "Envelope Analysis" in the Discussion:
  1. Even if you don't code it, mention it.
  2. Action: In your "Future Work" section, explicitly state: "Future iterations should implement Envelope Analysis (Hilbert Transform) to demodulate the impulsive impacts, which is superior to simple spectral analysis for early fault detection."
Summary: This is a solid, well-executed report. To get top marks, you need to show you understand why your current simple model is limited and suggest the specific advanced tools (Kurtosis/Enveloping) that would fix it.